## Slide 1: PoP-ECC: Robust and Flexible Error Correction against Multi-Bit Upsets in DNN Accelerators
Taewon Park†, Saeid Gorgin*, Dongwhee Kim†, Jaeho Shin*, Michael B. Sullivan††, and Jungrae Kim*
†Samsung Electronics, *Sungkyunkwan University, ††NVIDIA

## Slide 2: Background & Motivation

## Slide 3: DNNs and Errors
Two types of errors
  Data errors:
  Small noises on the input data
  Bit errors:
  Random bit flips during storage

## Slide 4: DNNs and Data Errors
DNNs inherently tolerate small data errors, facilitating quantization.
Quantization schemes
  Layer-wise vs. channel-wise
    Channel-wise quantization provide better accuracy.
A. Gholami, S. Kim, Z. Dong, Z. Yao, M. W. Mahoney, and K. Keutzer,​ “A survey of quantization methods for efficient neural network inference,” 2021. [Online]. Available: https://arxiv.org/abs/2103.13630​
Layer 1
Layer N
Layer 2
Input: x
Output: y
Filter 1
Filter 2
Filter N
Layer-wise
Channel-wise
Model | FP32 | 8-bit Quantization | 
 |  | Layer | Channel
ResNet50 |  |  | 
DenseNet169 |  |  | 
Inception V3 |  |  | 
MobileNet V2 |  |  | 
EfficientNet-B2 |  |  | 
RegNetX-8GF |  |  | 
Average |  |  | 
Model | FP32 | 8-bit Quantization | 
 |  | Layer | Channel
ResNet50 |  |  | 
DenseNet169 |  |  | 
Inception V3 |  |  | 
MobileNet V2 |  |  | 
EfficientNet-B2 |  |  | 
RegNetX-8GF |  |  | 
Average |  |  | 
A comparison of accuracy degradation between layer- and channel-wise quantization (uniform quantization)

## Slide 5: DNNs and Bit Errors
Bit errors on most significant bits affect DNN accuracy by changing the data value significantly.
G. Li et al., "Understanding Error Propagation in Deep Learning Neural Network (DNN) Accelerators and Applications," SC17: International Conference for High Performance Computing, Networking, Storage and Analysis, 2017, pp. 1-12.
Classification Error (%)
Bit Error Ratio (channel-wise quantization on ResNet50)
(No error)

## Slide 6: Prior Work on SRAM Protection
Many DNN processors have large SRAMs to store coefficients and activations.
Prior work on SRAM protection:
  Weight Nulling [1]
  In-place Zero-space ECC [2]
  Value-aware Parity Insertion ECC [3]
[3] S.-S. Lee and J.-S. Yang, “Value-Aware Parity Insertion ECC for Fault Tolerant Deep Neural Network,” (DATE), 2022.
[1] M. Qin et al., “Robustness of Neural Networks against Storage Media Errors,” 2017. (https://arxiv.org/abs/1709.06173)
[2] H. Guan et al., “In-place zero-space memory protection for CNN,” (NIPS), 2019.
Weight Nulling
In-place Zero-space
Value-aware Parity Insertion ECC

## Slide 7: Prior Work on SRAM Protection
Many DNN processors have large SRAMs to store coefficients and activations.
Prior work on SRAM protection:
  Weight Nulling [1]
  In-place Zero-space ECC [2]
  Value-aware Parity Insertion ECC [3]
[3] S.-S. Lee and J.-S. Yang, “Value-Aware Parity Insertion ECC for Fault Tolerant Deep Neural Network,” (DATE), 2022.
[1] M. Qin et al., “Robustness of Neural Networks against Storage Media Errors,” 2017. (https://arxiv.org/abs/1709.06173)
[2] H. Guan et al., “In-place zero-space memory protection for CNN,” (NIPS), 2019.
Weight Nulling
In-place Zero-space
Value-aware Parity Insertion ECC
Mostly can correct single-bit errors!

## Slide 8: Prior Work on SRAM Protection
However, technology scaling and lower supply voltage raise Multi Cell Upset (MCU) rates in SRAM.
Supply Voltage()
Multi Cell Upset rate
SP SRAM
TP SRAM
Classification Error (%)
Double Adjacent Error Ratio
(No error)

## Slide 9: Prior Work on SRAM Protection
However, technology scaling and lower supply voltage raise Multi Cell Upset (MCU) rates in SRAM.
Supply Voltage()
Multi Cell Upset rate
SP SRAM
TP SRAM
Classification Error (%)
Double Adjacent Error Ratio
(No error)
This necessitates utilizing an mechanism to correct MCUs.

## Slide 10: Error Correction Codes (ECC)
A common solution to DNN reliability is using ECC.
ECC Encoder
Data
Parity
Data
Parity

## Slide 11: Error Correction Codes (ECC)
A common solution to DNN reliability is using ECC.
ECC Decoder
Data
Corrupted Data
Data
Parity
Parity
Data
ECC Encoder
Parity

## Slide 12: Error Correction Codes (ECC)
A common solution to DNN reliability is using ECC.
However, the large SRAMs in DNN accelerators make the 12.5% ECC overhead costly, while offering limited protection against MCUs.
ECC Decoder
Data
Corrupted Data
Data
Parity
Parity
Data
ECC Encoder
Parity

## Slide 13: Error Correction Codes (ECC)
A common solution to DNN reliability is using ECC.
However, the large SRAMs in DNN accelerators make the 12.5% ECC overhead costly, while offering limited protection against MCUs.
ECC Decoder
Data
Corrupted Data
Data
Parity
Parity
Data
ECC Encoder
Parity
A novel scheme is required to reduce redundancy and provide strong memory protection for target MCUs.

## Slide 14: Parities of Parities ECC (PoP-ECC)

## Slide 15: PoP-ECC
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
W0
W1
W7
A block with 8 weights

## Slide 16: PoP-ECC
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
1st-level ECC encoding
W0
W1
W7
VP0
VP1
VP7

## Slide 17: PoP-ECC
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
  Second level: protects VPs using Parities of Parities (PPs) via RS encoding.
1st-level ECC encoding
2nd-level ECC encoding
W0
W1
W7
PP0
PP1
PP2
PP3
VP0
VP1
VP7

## Slide 18: PoP-ECC
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
  Second level: protects VPs using Parities of Parities (PPs) via RS encoding.
1st-level ECC encoding
2nd-level ECC encoding
W0
W1
W7
W0
W1
W7
PP0
PP1
PP2
PP3
VP0
VP1
VP7
Encoding

## Slide 19: PoP-ECC
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
  Second level: protects VPs using Parities of Parities (PPs) via RS encoding.
1st-level ECC encoding
1st-level ECC encoding
2nd-level ECC encoding
W0
W1
W7
W0
W1
W7
PP0
PP1
PP2
PP3
VP0
VP1
VP7
PP0
PP1
PP2
VP7
PP3
VP0
VP1
Encoding

## Slide 20: PoP-ECC
VP0
VP1
VP7
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
  Second level: protects VPs using Parities of Parities (PPs) via RS encoding.
1st-level ECC encoding
1st-level ECC encoding
2nd-level ECC encoding
W0
W1
W7
W0
W1
W7
PP0
PP1
PP2
PP3
VP0
VP1
VP7
PP0
PP1
PP2
VP7
PP3
VP0
VP1
2nd-level ECC decoding
Encoding

## Slide 21: PoP-ECC
W0
W1
W7
1st-level ECC decoding
VP0
VP1
VP7
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
  Second level: protects VPs using Parities of Parities (PPs) via RS encoding.
1st-level ECC encoding
1st-level ECC encoding
2nd-level ECC encoding
W0
W1
W7
W0
W1
W7
PP0
PP1
PP2
PP3
VP0
VP1
VP7
PP0
PP1
PP2
VP7
PP3
VP0
VP1
Encoding
2nd-level ECC decoding

## Slide 22: PoP-ECC
W0
W1
W7
1st-level ECC decoding
VP0
VP1
VP7
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
  Second level: protects VPs using Parities of Parities (PPs) via RS encoding.
1st-level ECC encoding
1st-level ECC encoding
2nd-level ECC encoding
W0
W1
W7
W0
W1
W7
PP0
PP1
PP2
PP3
VP0
VP1
VP7
PP0
PP1
PP2
VP7
PP3
VP0
VP1
Encoding
2nd-level ECC decoding
Decoding

## Slide 23: PoP-ECC
W0
W1
W7
1st-level ECC decoding
VP0
VP1
VP7
PoP-ECC is a strong and flexible two-level ECC scheme to prevent severe memory errors.
  First level: extracts Virtual Parities (VPs) from the weights.
  Second level: protects VPs using Parities of Parities (PPs) via RS encoding.
1st-level ECC encoding
1st-level ECC encoding
2nd-level ECC encoding
W0
W1
W7
W0
W1
W7
PP0
PP1
PP2
PP3
VP0
VP1
VP7
PP0
PP1
PP2
VP7
PP3
VP0
VP1
Encoding
2nd-level ECC decoding
Decoding
Extracting a VP from raw data can be customized to the target MCUs.
PoP-ECC operates efficiently across various precisions and sizes.

## Slide 24: Quantization & PoP-ECC (Q+PoP)

## Slide 25: Q+PoP
Q+PoP combines the high accuracy of channel-wise quantization with the robustness of PoP-ECC without extra SRAM for ECC redundancy.
Quantization (Channel-wise)
Q+PoP
PoP-ECC (strong & flexible )

## Slide 26: Q+PoP encoding process
Without loss of generality, Q+PoP reduces FP32 to INT6 using channel-wise quantization.
Trained FP32 Weight
W7
W1
W0

## Slide 27: Q+PoP encoding process
Without loss of generality, Q+PoP reduces FP32 to INT6 using channel-wise quantization.
6b
6b
Channel-wise Quantization
W0
W1
W7
6b
Trained FP32 Weight
W7
W1
W0
Quantized Weight

## Slide 28: Q+PoP encoding process
In the first stage, a 4-bit Virutual Parity (VP) is generated from the 6-bit weight.
  The generated 4-bit VP is designed to correct all single- and double-bit errors in the upper 5-bits of the quantized weight.
In the second stage, PoP-ECC utilizes RS code to protect VPs on a symbol basis.
  Q+PoP applies 4-bit RS encoding to the eight VPs to generate 4 PPs.
6b
6b
1st-level ECC encoding
Channel-wise Quantization
2nd-level ECC encoding
W0
W1
W7
6b
4b
4b
4b
4b
6b
6b
6b
W0
W1
W7
PP0
PP1
PP2
PP3
VP0
4b
VP1
4b
VP7
4b
Trained FP32 Weight
W7
W1
W0
Parity of Parity
Virtual Parity
Quantized Weight

## Slide 29: Q+PoP decoding process
On receiving the erroneous block, PoP-ECC first regenerates VPs using the same generator matrix as the encoding.
6b
W0
W1`
6b
6b
W7`
PP0
4b
PP1
4b
PP2
4b
PP3
4b

## Slide 30: Q+PoP decoding process
(12, 8) RS code decoding can correct two erroneous 4-bit VPs with four 4-bit PPs.
After restoring the VPs, PoP-ECC utilizes the VPs to restore the weights.
6b
W0
W1`
6b
6b
W7`
PP0
4b
PP1
4b
PP2
4b
PP3
4b
6b
6b
6b
W0
W1
W7
VP0
VP1
1st-level ECC decoding
VP7
PP0
PP1
PP2
VP7'
PP3
VP0
VP1'
2nd-level ECC decoding
1st-level ECC encoding

## Slide 31: Evaluation

## Slide 32: Evaluation
We implemented WN, VAPI, and Q+PoP in the PyTorch framework.
Methodology |  |  |  | 
Mem. protection schemes | DNN Models | Error Injection | Input dataset | Error ratios
WN VAPI Q+PoP | ResNet50 DesneNet169 Inception V3 MobileNet V2 EfficientNet-B2 RegNetX-8GF | SE (Single Error) DAE (Double Adjacent Error) | ISLVRC-2012 (50,000 validation images) | 10-5 to 10-1

## Slide 33: Evaluation
We implemented WN, VAPI, and Q+PoP in the PyTorch framework.
Methodology |  |  |  | 
Mem. protection schemes | DNN Models | Error Injection | Input dataset | Error ratios
WN VAPI Q+PoP | ResNet50 DesneNet169 Inception V3 MobileNet V2 EfficientNet-B2 RegNetX-8GF | SE (Single Error) DAE (Double Adjacent Error) | ISLVRC-2012 (50,000 validation images) | 10-5 to 10-1
Accuracy
  Accuracy without errors (shows the impact of quantization)
Reliability
  Accuracy with errors
Hardware overheads

## Slide 34: Base Top-1 classification Accuracy
Q+PoP shows an average of 1.07% degradation.
Model | FP32 | WN | VAPI | Q+PoP
ResNet50 |  |  |  | 
DenseNet169 |  |  |  | 
Inception V3 |  |  |  | 
MobileNet V2 |  |  |  | 
EfficientNet-B2 |  |  |  | 
RegNetX-8GF |  |  |  | 
Average |  |  |  | 
Model | FP32 | WN | VAPI | Q+PoP
ResNet50 |  |  |  | 
DenseNet169 |  |  |  | 
Inception V3 |  |  |  | 
MobileNet V2 |  |  |  | 
EfficientNet-B2 |  |  |  | 
RegNetX-8GF |  |  |  | 
Average |  |  |  | 
WN provides almost the same accuracy as the pretrained FP32 weights.
VAPI sacrifices accuracy significantly (up to 80.51%) in our evaluation.

## Slide 35: Reliability against Single-Errors
Q+PoP can provide higher accuracy than VAPI, for lower SBUs (< 10-5).
Q+PoP can tolerate the highest BER of up to near 3x10-3.
(d) MobileNet V2
(e) EfficientNet-B2
(f) RegNetX-8GF
(a) ResNet50
(b) Densenet169
(c) Inception V3
The accuracy of WN decreases quickly as the ratio approaches 10-4.
(No error)

## Slide 36: Reliability against Double-Adjacent Errors
Q+PoP can tolerate:
  up to 10-3 by correcting up to two DAEs within a 64-bit block.
  up to 31.62x higher *maximum DAE ratio than VAPI.
(d) MobileNet V2
(e) EfficientNet-B2
(f) RegNetX-8GF
(a) ResNet50
(b) Densenet169
(c) Inception V3
* Maximum DAE ratio is that which does not reduce DNN accuracy by 0.1 percentage point than error-free cases.
WN cannot detect double-bit errors within a weight even at lower DBUs (<10-5).
At 10-3, VAPI cannot protect DNN accuracy.
(No error)

## Slide 37: Hardware Costs
Hardware Cost | Speed | Area | Power
PoP-ECC Encoder | 0.65ns | 92um2 (0.3K NAND2 gates) | 0.08mW
PoP-ECC Decoder | 1.56ns | 1760um2 (6K NAND2 gates) | 1.2mW
Synthesis Set-up
  Compiler : Synopsys design compiler
  Logic libraries : UMC 28nm SVT library.

## Slide 38: Conclusion

## Slide 39: Conclusion
Technology scaling => Rising soft error rates “Multi-Cell Upsets (MCUs) now common”
Up to 31.62× better DAE tolerance Higher accuracy with negligible delay, area, and power cost

## Slide 40: Conclusion
Our Solution – PoP-ECC Robust and flexible Two-level ECC: Virtual Parities + Parities of Parities Effectively mitigates MCUs with minimal overhead
p to 31.62× better DAE tolerance Higher accuracy with negligible delay, area, and power cost
Technology scaling => Rising soft error rates “Multi-Cell Upsets (MCUs) now common”

## Slide 41: Conclusion
Our Solution – PoP-ECC Robust and flexible Two-level ECC: Virtual Parities + Parities of Parities Effectively mitigates MCUs with minimal overhead
Q+PoP Combines PoP-ECC + Channel-wise quantization Tailored for efficient DNN protection
Up to 31.62× better DAE tolerance Higher accuracy with negligible delay, area, and power cost
Technology scaling => Rising soft error rates “Multi-Cell Upsets (MCUs) now common”

## Slide 42: Conclusion
Our Solution – PoP-ECC Robust and flexible Two-level ECC: Virtual Parities + Parities of Parities Effectively mitigates MCUs with minimal overhead
Q+PoP Combines PoP-ECC + Channel-wise quantization Tailored for efficient DNN protection
Up to 31.62× better DAE tolerance Higher accuracy with negligible delay, area, and power cost
Technology scaling => Rising soft error rates “Multi-Cell Upsets (MCUs) now common”